First Slide Example
Floating-Point Numbers
Marc Andrysco

---
Overview
- Floating-Point Numbers
  - Scientific-notation
  - IEEE-754 representation
- Denormal Number Timing Attack
  - SVG transforms
  - Timing channels
  - Stealing pixels

---
Floating-Point Format
- Integers
- Fixed-point numbers
- Floating-point numbers
- Precision and rounding

---
Default Example
On Spelling
From grade school grammar:
'i' before 'e' *
* except after 'c' ✢
✢ or when sounded as 'a' ❊
as in neighbor or weigh
❊ still sometimes wrong
like 'species' or 'caffeine'

---
Integers
-2
-1
1
2
3
4
5
0
- Take up whole number spots on the number line
- Space between each is always 1
- 32-bit integers have 2^32 unique points
  - Signed range [-2147483648, 2147483647]
- The number line can wrap around the globe

---
Fixed-Point Numbers
-0.01
0.01
0.02
0.03
0
- Integers scaled by a constant factor
- Space between points is always constant
- Useful for fixed decimal values like currency
- 32-bit numbers have 2^32 unique points
  - Example range [-21474836.48, 21474836.47]

---
Scientific Notation
- Contains a “floating” decimal point
  - 1.2 × 10-2 same as 0.012 × 100
- Easy to represent large and small values
  - 1.6162 × 10-35, 6.02 × 1023
- Made up of two pieces
        1.2 10-2
  - Significand/mantissa/fraction
  - Exponent

---
Normal Form
0.01616 × 10-33 1.616 × 10-35 1616.0 × 10-38
- Non-zero, single digit left of the decimal
  - Called normal or normalized
- Non-conforming forms are “denomalized”
  - All denormalized numbers can be made normal ✢
    ✢ Except zero, infinity...

---
Fixed Precision
- Fix the number of of digits
  - Always use normal form
- Ex: 3 significand digits, 2 exponent digits
  - Maximum number 9.99×1099
  - Minimum (non-zero) 1.00×10-99
- Missing zero!
  - It has no normal form

---
Floating-Point Range
1.0
2.0
4.0
0
- Space between floats vary
- Allows for an enormous range
  - Max value of 9.99×1099
    - Times larger than the observable universe
    - Next smaller value, 9.98×1099 is a difference of 0.01×1099
  - Min value of 1.00×10-99
    - 1.6×1064 times smaller than Planck length

---
Rounding
- Not all numbers have finite representations
  - The fraction 1/3 cannot be written in decimal
- Round to the nearest representation
  - 1/3 would be 3.33×10-1
  - Round to even if directly in between representations
- Other rounding modes
  - Round toward zero, infinity, -infinity

---
IEEE-754 Floats
- IEEE-754 standard
- Special values
- Denormalized numbers

---
IEEE-754 Standard
- IEEE-754 specifies standard formats for floats
  - Binary32: “single-precision” ; float in C
  - Binary64: “double-precision” ; double in C
- Like scientific-notation, uses binary
  - 1.0101110001b×2101b
  - Normal forms, first digit must be 1

---
Single-Precision Float
- 1-bit sign, 8-bit exponent, 23-bit fraction ✢
- Maximum: 3.402823466×1038
- Minimum: 1.175494351×10−38 ❊
  ✢ Special forms for other numbers (zero, infinity...)
  ❊ That's sometimes lie

---
Double-Precision Float
- 1-bit sign, 11-bit exponent, 52-bit fraction ✢
- Maximum: 1.7976931348623157×10308
- Minimum: 2.2250738585072014×10−308
  ✢ Same exceptions apply

---
Float Representation
- Fraction starts with 1 (ex: 1.0100...)
- Exponent is biased by 127
  - Example as above: 0111100b – 127 = 124 – 127 = -3
  - Makes floats better ordered

---
Special Values
- Zero – all exponent and fraction bits are zero
  - Sign bit can be negative for -0.0
- Infinity – all exponent and fraction bits are one
  - Sign bit can be negative for -Infinity
- NaN – exponent is ones, fraction is not all ones
  - Have many NaN representations including -NaN

---
Denormalized Numbers
- Occurs when all exponent bits are zero
  - No longer given that the first fraction bit is one
  - Takes the form 0.000110b×2-126
- Larger representable range
- Extreme loss of precision
- Can have an extreme loss of performance
- Frequently omitted (e.g. GPUs)

---
Denormalized Range
- Numbers smaller than the “minimum”
- Single-precision floats
  1.175494351×10−38 to 1.4012985×10−45
- Double-precision floats
  2.2250738585072014×10−308 to 5×10−324

---
Firefox Timing Attack
- Attack Overview
- Timing Channel
- Pixel Extraction

---
Attack Overview
- Create a legitimate website
- In the page, hide an <iframe> to a target website that contains private data (i.e. chase.com)
- Use a timing channel to create an image copy of the <iframe> contents
- Extract private information from the image

---
Timing Channel
- Hiding an <iframe> in a website is easy
- Apply image transformation that vary based on the <iframe> contents
- Quick transformation = the <iframe> is white
- Slow transformation = the <iframe> is black

---
SVG Transforms
- SVG standard defines transformations on SVG elements
- HTML5 allows transformations as a CSS style
  - applies to any HTML element
- Ex: gaussian blur, greyscale, sepia, specular and diffuse lighting, image composition, ...

---
Example Transforms

---
SVG Computation
- Transform act on input image to an output image
  - Applying to HTML elements are flattened to images
- Images are RGBA pixmaps
  - Each color channel is an 8-bit unsigned integer
- Some transforms internally compute using floating-point arithmetic
- These computation give us our timing channel

---
Denormalized Performance
- Many operations on denormalized numbers are ~75 times slower!
- The operation a∗b=c is slow if
  - a, b, or c is denormalized
  - And no values are zero

---
Convolution Filter
- Inputs a kernel matrix M
- The kernel matrix is multiplied against every input coordinate to produce the output pixel

---
Convolution Filter

---
SVG Convolution
- Includes an arbitrary divisor
- Using a 1x1 kernel, each pixel is computed as
  - y is the output pixel
  - x is the input pixel
  - k is the kernel matrix
  - d is the divisor

---
Denormal Convolution
- Uses single-precision floats
- No constant can be smaller than 0.001
  k = 0.001
  d = 1.0×1038
- If x = 0, then y = 0
- If x = 255, then y = 2.55×10-39
  - y is denormal!
- Computed for every color channel of every pixel

---
Denormal Timing Signal
- Apply malicious convolution filter to <iframe>
- If the filter is applied quickly, <iframe> is black
- If the filter is applied slowly, <iframe> is white
- Measure timing with requestAnimationFrame
  - Executes callback once finished rendering
  - Tied to the refresh rate of the monitor (60 Hz)

---
Denormal Pixel Extraction
- Use SVG transforms to isolate a single pixel
- Apply timing attack to a single pixel
- Iterate over all pixels of the target iframe
- Very slow at ~20ms per pixel
  - 2.7 hours to read an 800x600 iframe

---
Full Attack
- Create a legitimate website (flash game)
- Hide an <iframe> to a target website (chase.com)
- Apply an convolution filter on the <iframe>
  - White pixels = slow
  - Black pixels = fast
- Use the timing data to read individual pixels
- Extract private information from the image (bank info)

---
Current Work
- Pixel Isolation
- Apply to Webkit
  - Webkit is accelerated using OpenCL
  - No denorms on GPUs
- Improve Attack Speed
  - Convolution transforms can perform letter detection
  - Test target for an entire letter at once
  - Should read a few characters per second

---
Questions

---
Shapes
Pre-defined Shapes
Here are some pre-defined shapes for your convenience: copy the shapes, copy their formatting, or use the LibO styles.
Green Dark
Green Bright
You may add your code examples, XML statements, or debug output here ;-)
Blue Dark
Blue Bright
Orange Dark
Orange Bright
Purple Dark
Purple Bright
Yellow Dark
Yellow Bright

---
Section Header Example
Section Header Example
You may add additional text here ...

---
Final Slide Example
Thank you …
- … for using this template!
- … for supporting LibreOffice!

---
Normalized Math
- Multiplication is easy
  - y×2z = a×2b × c×2d
  - y = a×c
  - z = b+d
  3.1×24 × 2.6×2-2
  3.1 × 2.6 = 8.06
  4 + -2 = 4
  8.06×22

---
Normalized Math
- Addition is harder
  - y×2z = a×2b + c×2d
  - y×2z = a×2b + c'×2b
  - y = a + c'
  - z = b
  3.1×24 + 2.6×23
  3.1×24 + 0.26×24
  3.1 + 0.26 = 3.36
  4 = 4
  3.36×24

---
Denormalized Math
- All operations are harder
  - Results may be outside representable range
  - Multiplication yields wildly denormalized results
  - Much slower on modern CPUs (Intel, AMD)
- Frequently omitted
  - GPUs round denormals to zero